## Slide 1
Understanding the Impacts of Renewable Energy and Infrastructure Loads on Food-Energy-Water Security in Remote Arctic Communities
American Geophysical Union Fall 2018 Meeting
Panel Session GC52B: The Food–Energy–Water System Nexus and Decision Support for Sustainability I
Paper number: GC52B-07
December 14, 2018
Presenting Author: Richard Wies1,2,3
Project Team: Srijan Aggarwal5, Aaron Dotson6, Craig Gerlach7, Daisy Huang3,4, Justus Karenzi1,2, Henry Penn7, Christopher Pike3, Daniel Sambor8, Erin Whitney3
University of Alaska Fairbanks - 1Electrical and Computer Engineering, 2Institute of Northern Engineering, 3Alaska Center for Energy and Power, 4Mechanical Engineering, 5Civil Engineering
6University of Alaska Anchorage - Civil Engineering
7University of Calgary – Arctic Institute of North America
8Stanford University - Civil and Environmental Engineering, Atmosphere/Energy Program
This work is supported by NSF Chemical, Bioengineering, Environmental and Transport Systems (CBET), Track 3 INFEWS program, Award # 1740075,
INFEWS/T3: Coupling infrastructure improvements to food-energy-water system dynamics in small cold region communities: MicroFEWs.

## Slide 2
OUTLINE
MicroFEWs Project Description
Research Questions
Alaska’s Remote Islanded Microgrids
Stakeholder Community Energy Systems
Energy Distribution Model/ Simulation
Lab Testing and Validation
Status and Path Forward

## Slide 3
MicroFEWS Project Description
Engage communities
Identify connections between renewables and FEWS infrastructure
Optimization of renewables driving FEWS loads
FEWS loads
  Food production
  Water treatment
  Modular systems
  Dispatchable?
Enhance FEW security in remote islanded microgrids
Coupling infrastructure improvements to food-energy-water system dynamics in small cold region communities: MicroFEWs

## Slide 4
MicroFEWS Project Description
Results for Community Planning
Results for Scientific Community
Research Questions:
1) What are the direct and indirect linkages and feedbacks between renewable energy generation and the local drivers of food, energy, and water (FEW) security in Arctic and Subarctic communities?
2) To what extent can combinations of renewable energy generation and FEW-related infrastructure energy loads be optimized to enhance FEW security in Arctic and Subarctic communities?

## Slide 5
Remote Islanded Microgrids
Firm generation
Intermittent generation
Energy storage
Demand Response

## Slide 6
Alaska’s Remote Islanded Microgrids
70 of ~200 Alaska RIMs use renewable energy sources
Alaska has ~12% of the worlds microgrids that incorporate grid scale renewable resources. (data from Navigant Research)

## Slide 7
Alaska Islanded Grid Realities
Harsh and changing climate
End of supply lines
Dispersed population
Limited road network
Icebreaker supported fuel delivery to Nome
Erosion from fall storms - Shishmaref
Limited fuel delivery on ice roads

## Slide 8
Alaska Islanded Grid Realities
High energy costs
Fragmented electric grid
Stranded resources
Diesel Generators:
Electric power in rural Alaska subsidized costs $0.50-$1.50/kWhr
Oil Stove:
Heating oil costs
$3.50 to $10/gallon
St. Paul Island Wind:
3-275 kW Vestas V17

## Slide 9
Cordova: Hydroelectric
Seasonal Demand Swing – Cordova, AK
Cordova Energy Mix (2011): 18 GWh Hydropower,10 GWh Diesel
781,000 Gal Diesel @ $3.55/gal = $2.77M Fuel bill
Cost of generation: Hydro: ~$0.06/kWh, Diesel: ~$0.35/kWh
Estimate: 3.8 GWh spilled hydro
Can some of the spilled hydro be recovered to displace diesel fuel?
Images: Inflatable hydroelectric dam at Powercreek
Current: Seasonal diesel off with hydroelectric;
Future: + battery energy storage (RADIANCE)
Seasonal variability: resources and demand
Lost potential (spilled hydro)
Load levelling / peak shifting
Energy storage (RADIANCE)

## Slide 10
Kongiginak: Wind  Heat System
20+ thermal electric stoves installed in elder and low income homes
Diesel off with wind + energy storage + distributed heating
VIDEO: https://www.youtube.com/watch?v=90n9ga3SOQQ
5 – 95 kW Windmatic direct drive turbines (30-40% wind penetration annually)

## Slide 11
Tanana: Biomass District
Heating System
Images: Top left: woody biomass boiler; Bottom right: woody biomass delivered and sold to community by residents along river
District heating:
Current: community buildings
Future: greenhouses
Woody biomass + biomass boiler + district heating

## Slide 12
Igiugig: Hydrokinetic Project
Ocean Renewable Power Company (75 kW Gorlov Turbine)
Diesel electric + Hydrokinetic
Diesel Powerhouse

## Slide 13
MicroFEWS Energy Distribution Model (EDM)
MODULAR SYSTEM LOADS
Lifewater Wastewater Treatment Module (350 W Max)
UAA In-home Water Reuse System (1.0 kW Max)
CropBox Hydroponic Module (14 kW Max)
INTERMITTENT RENEWABLES
Hydrokinetic
(In-River)
Wind
Solar PV
DISPATCHABLE AND INTERUPTIBLE LOADS
Food Production
Water Treatment
Modular Systems
OPTIMIZE
ENERGY DISTRIBUTION & DISPATCH
FIRM ENERGY SOURCES
Diesel Electric
Hydroelectric (Dam)
ENERGY STORAGE SYSTEMS
Battery
Flywheel
Photo Credit: Steffes Corporation
Electric Thermal Heaters
Inverter

## Slide 14
Parameters for EDMs

## Slide 15
Example 1: Solar PV + Diesel + Battery  Water Treatment (250 gal/day)
Water Extracted: 208 gal/day
Water Treated: 250 gal/day

## Slide 16
Example 1: Solar PV + Diesel + Battery  Water Treatment (500 gal/day)
Water Extracted: 475 gal/day
Water Treated: 500 gal/day

## Slide 17
Example 2: Wind + Diesel  Modular Loads (Water Reuse + CropBox)

## Slide 18
Example 2: Wind + Diesel  Modular Loads (Water Reuse + CropBox)

## Slide 19
Example 3: Passive Solar + Diesel  Greenhouse

## Slide 20
Laboratory Testing and Validation of EDMs
320 kW Cat C-15 diesel, w/ Woodward EasyGen 3200
100 kW Wind Turbine Simulator (induction)
100 kW Solar PV Simulator w/ 25 kW Fronius Inverter
313 kW ABB PCS100 Inverter
540 VDC/1000 Ah Absolyte VRLA Battery
Two 250 kW, 200 kVar LoadTech Loadbanks
1000+ channel custom data collection
Power System Integration Laboratory:
Bench Testing: Water Treatment
Modular Loads: Water Reuse, CropBox, Lifewater
Power Systems Integration Laboratory: FEW Scenarios

## Slide 21
Status and Path Forward
Communities (Remote Islanded Microgrids)
  Stakeholder meeting and community visits
  Document energy systems and FEW infrastructure
  Collect data (in progress: full year)
Energy Distribution Models and Lab Testing
  Renewable Generation  Dispatchable FEW Demand
  Optimize FEW connections
  Test FEW components, modular systems, and scenarios
Develop FEW Infrastructure Planning Tool
Integrate EDMs with FEW Infrastructure Planning Tool

## Slide 22
Thank you
Richard W. Wies, PhD, PE
Professor
Electrical and Computer Engineering
College of Engineering and Mines
Alaska Center for Energy and Power
University of Alaska - Fairbanks
Tel: (907) 474-7071
E-mail: rwwiesjr@alaska.edu
For more information:
Friday, Dec. 14, 1:40-6pm; Poster GC53F-1007: FEW SYTEM ASSESSMENT OF ONSITE WATER REUSE IN REMOTE ALASKA, Aaron Dotson, Taylor Ferguson, Richard Wies, Erin Whitney, Christopher Pike, Amanda Setiawan
This work is supported by NSF Chemical, Bioengineering, Environmental and Transport Systems (CBET), Track 3 INFEWS program, Award # 1740075,
INFEWS/T3: Coupling infrastructure improvements to food-energy-water system dynamics in small cold region communities: MicroFEWs.